Interface Electronics
- Connect real-world signals to microcontrollers
- User inputs
  - Switches, buttons
  - Analogue values (light, temperature, speed, etc.)
  - ”Dangerous” interfaces
- Control outputs
  - Motors, lights, valves, speakers

---
Interfacing Basics
- Make ”outside data” safe for microcontroller
  - Known values presented to input
  - Voltage swing within safe levels
  - Protect against ESD/RFI

---
Simple Switch Input
- R1 is a pull-up resistor
- Presents a logic '1' to input when switch not pressed
- Switch ”shorts” input to ground
- Switch pressed = logic '0'
- No ESD protection

---
Better Switch Input
- Diodes short high voltages to supply rails
  - (almost every microcontroller pin has small versions of this internally)
- R2 limits current and can help increase RFI

---
Voltage Divider
- Voltage at input =
  V+ * R2 / (R1 + R2)
- Select R1,R2 to ensure low enough voltage to be seen by microcontroller as a logic '0'
  - e.g. R1=10k, R2=1k makes V = 5*1/11 = 0.45V

---
Scaling with a Voltage Divider
- e.g. Want to monitor car battery voltage (range 0-16V)
- Max ADC input = 5V
- Need approx ¼ scale
- R1=16.5k, R2=7.5k
- Add protection diodes
http://focus.ti.com/docs/toolsw/folders/print/volt-divider-calc.html

---
Optical Isolation
- Until now, microprocessor has been at the same potential as the input signal
- Fine for battery powered circuits or low-voltage interfacing
- Optical isolation very easy for digital signals

---
Optical Isolation
- When LED is on, transistor conducts
  - Input = Logic '0'
- Hundreds of varieties of optos. Important parameters:
  - Isolation Voltage
  - Input type (AC or DC)
  - Current Transfer Ratio (CTR)

---
Montor AC voltage
- R2, R3 limit current (need about 20mA for LED)
  - R = V/I = 170/.02 = 8500 ohms total (4.7k each)
- Fuse protects you
- LED1 provides voltage path for -ve half of AC

---
Monitor AC Voltage
- Input will be 60Hz square wave
- Useful for time base
- If you want a steady signal, you must filter
AC Line
LED on
off
on
off
Microcontroller Input

---
Filtering Inputs
- Generally speaking ALL inputs must be filtered
  - Can be filtered in software or in hardware
  - Software = less hardware, but more complexity
  - Hardware = more robust, harder to adjust
- Never hook inputs to interrupt lines without hardware filtering!
  - Noisy inputs cause a storm of interrupts and the controller has no means of recovering

---
Basic 1st Order (low-pass) filter
- Capacitors resist a change in voltage
- 1st order filter reduces signal amplitude by half every time frequency doubles
- ”Slows down” input
  - high/low threshholds are ”stretched out”
f rsub{c} = {1} over {2 %pi R C}
http://www.muzique.com/schem/filter.htm

---
Filter AC Line Input
- R4/C1 form 1st order low-pass filter
  - Cutoff frequency (Fc) as shown is 16Hz
  - Provides active-low signal when AC is present
- R4/C1 with 8200Ω / 0.1uF gives ~200Hz cutoff
  - Useful filter for timing interrupt

---
Analog Signals
- Bringing analog signals into microcontroller have different requirements
  - Accuracy over sense range
    - Actual 1V = measured 1V?
  - Linearity
    - If 0.5V = 50 counts, does 1V = 100,1.5V = 150?
  - Input impedance
    - Signals usually weak, so measuring may have a negative effect on the actual signal measured
- Conditioning circuitry can affect/improve all of these parameters

---
Operational Amplifier
- Basic building block of analog circuitry
- Inputs are EXTREMELY high impedance
  - Very little effect on circuit being measured
- Output is LOW impedance
  - Easily drives most loads

---
Operational Amplifier
- Connections determine ”operation”
  - Generally speaking, moves output to make inputs equal
  - Not really useful without feedback
  - Numerous functions
    - Sum, Difference, Multiply signals
    - Integrate, Filter signals
    - Buffer and Scale signals
    - Amplify signals

---
Buffering an input
- Most common use with microcontrollers
- Measured signal is very lightly loaded
- Op-amp can easily drive ADC input on microcontroller
- Vout = Vin

---
Amplification
- Positive and Negative
- Different forumula for gain for each
- Be mindful of signal levels with unipolar supplies
  - Can't make output go above +V or below -V
  - Usually requires bias
V_{out} = (1 + {R2} over {R1}) V_{"in"}
V_{out} = -{{R2} over {R1}} V_{"in"}
http://www.national.com/an/AN/AN-31.pdf

---
Biasing
- Most microcontrollers only measure positive analog voltages
- In order to measure a
  bipolar audio source
  (e.g. audio) it is
  necessary to bias the
  input so that
  0V = some middle
  voltage to the ADC
V_{out} = V_{"in"} (1 + R2 over{R1 + R3}) + V^"+"(R3 over{R3 + R4})

---
Biasing – Measuring Audio
- C1 blocks any DC present in input signal
- Gain of +2ish, C3 attenuates gain at higer freq.
- R5/C2 low-pass filter at Fc=3400Hz
- R3/R4 set bias point at mid-supply, C4 stores

---
Measuring Current
- Easiest method is to use a shunt
  - Since I=V/R, measuring the voltage developed across a known resistance gives the current flowing through that resistance
  - Measurement circuit is not isolated from current flow
  - DO NOT USE to measure outlet current!

---
Measuring Current - Example
- Op-amp configured as a differential amplifier
- Subtracts voltage at either side of Rs and amplifies the difference
- RS = shunt resistance
  - Very low value, possibly high wattage!
V_{R_shunt} = I_{motor} R_shunt
V_{out} = V_{RS} RF over{R1}
R1 = R2

---
Output Interfacing
- Variety of methods
  - Direct I/O drive
  - Transistors, FETs
  - Relays
  - Thyristors (SCRs, Triacs)
- Microcontroller outputs have limited drive
  - Most do not have any protection from overdrive

---
Direct I/O Drive
- Easy to drive most LEDs
- I = V/R
  - 330 ohms is a good default value
  - 15mA@5V, 10mA@3.3V
- Most I/O limited to about 20mA drive for entire port

---
Multiplexing
- ”re-using” I/O in combinations
- Common for large LED arrays or 7-segment displays
- More complex method known as ”charlieplexing”
  - Even more combinations

---
Driving Bicolour LEDs
- GP0=1 GP2=0 lights one way
- GP0=0 GP2=1 lights the other
- Toggle 10/01 to light both
- GP0=1 for one way, GP0=0 for the other, GP0=input for off
- Not recommended

---
Driving Transistors
- A small current into the base allows a large current to flow in collector
- Vbe must be > 0.7V
- Transistors are current-controlled, not voltage controlled
Collector
Base
Emitter

---
Common Emitter Transistor
- Most common configuration
- When I/O raised to '1', current flows into base
- Transistor turns on, lights LED

---
Analysis
- GP2=5V, Vbe=0.7V
- 4.3/1000 = ~4mA into base
- Assume V+ = 24V, 2V drop across LED, Vce=1.4V
- 20.6/100 = ~200mA available for LED

---
Pulse Width Modulation
- Digital output, but a time-averaged output gives an analog output
- Output filter determines performance

---
The H-Bridge
- Four transistors
  - 2 NPN, 2 PNP
- Careful control allows current to flow across ”H” in either direction
- Simplified schematic

---
H-Bridge Application
- Measure motor current with shunt + follower
- Assume V+ = 24V, Vce=1.4V
- V = IR, when motor draws 2A, voltage across shut is 4V
  - Use to detect stall

---
Relays
- Easy to drive (use a transistor)
- Be careful of voltage spike when relay coil opens!
- Reverse-biased diode helps protect against spike

---
Relays
- Alternative protection method
- Also protects transistor against supply transients
- R2 is good practise for all transistor circuits
  - Helps prevent noise from switching Q1 on

---
SCRs and Triacs
- Generally used to control AC voltages
- Triac essentially two SCRs in reverse-parallel
- Not absolutely necessary, but good practise to use with optoisolator

---
Better Triac circuit
- Adds Snubberring
  - (helps prevent false triggering)
  - More robust circuit
  - In-use in industry

---
Interface Electronics
Thank you!